## Slide 1: Unit-1 Fundamentals of Digital System
krunal.vyas@darshan.ac.in
9601901005
Computer Science & Engineering
Prof. Krunal D Vyas
Digital Fundamentals (DF)
DU #2101CS303

## Slide 2

Looping
Outline
  Logical Gates
  Number systems
  Binary arithmetic operations
  Complements arithmetic
  Binary Codes

## Slide 3: Logical Gates
Section - 1

## Slide 4: Logic Gates
Most basic logical unit of the digital system is gate circuit.
Types of gate circuits are as follows
  AND Gate
  OR Gate
  NOT Gate (Inverter)
  NOR Gate
  NAND Gate
  XOR Gate
  XNOR Gate

## Slide 5: 1. AND Gate
AND Gate has an output which is normally at logic level “0” and only goes “HIGH” to a logic level “1” when ALL of its inputs are at logic level “1”
A
B
C
Logic Notation
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table
2-input AND Gate

## Slide 6: 2. OR Gate
OR Gate or Inclusive-OR gate has an output which is normally at logic level “0” and only goes “HIGH” to a logic level “1” when one or more of its inputs are at logic level “1”.
A
B
C
Logic Notation
Truth Table
2-input OR Gate
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 7: 3. NOT (Inverter) Gate
NOT gate has an output which is always opposite to input level.
A
C
Logic Notation
Truth Table
Inverter Gate
A | C
0 | 1
1 | 0

## Slide 8: 4. NOR Gate
NOR Gate is an OR gate followed by an inverter.
NOR Gate has an output which is normally at logic level “1” and only goes “LOW” to a logic level “0” when one or more of its inputs are at logic level “1”.
A
B
C
Logic Notation
Truth Table
2-input NOR Gate
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 9: 5. NAND Gate
NAND Gate is an AND gate followed by an inverter.
NAND Gate has an output which is normally at logic level “1” and only goes “LOW” to a logic level “0” when ALL inputs are at logic level “1”.
A
B
C
Logic Notation
Truth Table
2-input NAND Gate
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 10: 6. Exclusive-OR (X-OR) Gate
X-OR gate that has 1 state when one and only one of its two inputs assumes a logic 1 state and has 0 state when all of its input are same.
Also known as anti-coincidence gate or inequality detector.
A
B
C
Logic Notation
Truth Table
2-input XOR Gate
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 11: 7. Exclusive-NOR (X-NOR) Gate
X-NOR gate that has 1 state when all of its input are same and has 0 state when one of its input has 0 state and other input is 1 state.
Also known as coincidence gate or equality detector.
A
B
C
Logic Notation
Truth Table
2-input XNOR Gate
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 12: NAND as Universal Gate
NOT using NAND
A
A’
A
B
(AB)’
((AB)’)’ = AB
AND using NAND
A
B
A’
(A’B’)’ = (A+B)
OR using NAND
B’

## Slide 13: NOR as Universal Gate
NOT using NOR
A
A’
A
B
(A+B)’
((A+B)’)’ = A+B
OR using NOR
A
B
A’
(A’+B’)’ = AB
AND using NOR
B’

## Slide 14: Number systems
Section - 2

## Slide 15: Common Number Systems
System | Base | Symbols | Used by Humans? | Used in Computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 16: Conversion among Bases
Possibilities
Example
Hexadecimal
Decimal
Octal
Binary
2510 = 110012 = 318 = 1916
Base

## Slide 17: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  The remainders read from bottom to top give the equivalent binary integer number.
Example - 1
12510 = ?2
2
125
1
2
62
0
2
31
1
2
15
1
2
7
1
2
3
1
2
1
1
0
12510 =
11111012
Example - 2
0.687510 = ?2
0.6875 x 2 =
1.3750
1
0.3750
+
0.3750 x 2 =
0.7500
0
0.7500
+
0.7500 x 2 =
1.5000
1
0.5000
+
0.5000 x 2 =
1.0000
1
0.0000
+
0.687510 =
0.10112
integer
fraction

## Slide 18: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right. Finally, Add the results.
Example - 1
1 0 1 0 1 1
1 x 20
1 x 21
0 x 22
1 x 23
0 x 24
1 x 25
+
+
+
+
+
1
2
0
1010112 =
0
32
+
+
+
+
+
4310
8
1010112 = ?10
Example - 2
11.112 = ?10
1 1 . 1 1
1 x 20
1 x 21
+
1
2
+
1 x 2-2
1 x 2-1
+
0.25
0.5
+
+
+
11.112 =
3.7510

## Slide 19: Decimal to Octal
Technique
  Divide by eight, keep track of the remainder
  The remainders read from bottom to top give the equivalent octal integer number.
Example - 1
12510 = ?8
8
125
5
8
15
7
8
1
1
0
12510 =
1758
0.687510 = ?8
0.6875 x 8 =
5.5000
5
0.5000
+
0.5000 x 8 =
4.0000
4
0.0000
+
0.687510 =
0.548
integer
fraction
Example - 2

## Slide 20: Octal to Decimal
Technique
  Multiply each digit by 8n, where n is the “weight” of the digit
  The weight is the position of the digit, starting from 0 on the right. Finally, Add the results.
Example - 1
7 2 4
4 x 80
2 x 81
7 x 82
+
+
7248 =
46810
4
16
448
+
+
7248 = ?10
43.258 = ?10
Example - 2
4 3 . 2 5
3 x 80
4 x 81
+
3
32
43.258 =
+
35.328110
5 x 8-2
2 x 8-1
+
0.0781
0.25
+
+
+

## Slide 21: Decimal to Hexa-Decimal
Technique
  Divide by sixteen, keep track of the remainder
  The remainders read from bottom to top give the equivalent hexadecimal integer number.
Example - 1
123410 = ?16
16
1234
2
123410 =
4D216
16
77
13=D
16
4
4
0
0.0312510 = ?16
0.03125 x 16 =
0.5000
0
0.5000
+
0.5000 x 16 =
8.0000
8
0.0000
+
0.0312510 =
0.0816
integer
fraction
Example - 2

## Slide 22: Hexa-Decimal to Decimal
Technique
  Multiply each digit by 16n, where n is the “weight” of the digit
  The weight is the position of the digit, starting from 0 on the right. Finally, Add the results.
Example - 1
A B C
C x 160
B x 161
A x 162
+
+
ABC16 =
274810
12 x 160
11 x 161
10 x 162
+
+
12
176
2560
+
+
ABC16 = ?10
43.2516 = ?10
Example - 2
4 3 . 2 5
3 x 160
4 x 161
+
3
64
43.2516 =
+
67.144510
5 x 16-2
2 x 16-1
+
0.0195
0.125
+
+
+

## Slide 23: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation
Example
Octal | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111
7058 = ?2
7 0 5
101
000
111
7058 =
1110001012

## Slide 24: Binary to Octal
Technique
  From given fractional point, group bits in threes to right and group bits in threes to left
  If, left with less than 3 bits at the end then stuff 0s to make it group of three
  Convert to octal digits
Example
1011010.1112 = ?8
1
011
001
1011010.1112 =
132.78
111
010
3
2
7
.

## Slide 25: Hexa-Decimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation
Example
Hexa-Decimal | Binary | Hexa-Decimal | Binary
0 | 0000 | 8 | 1000
1 | 0001 | 9 | 1001
2 | 0010 | A | 1010
3 | 0011 | B | 1011
4 | 0100 | C | 1100
5 | 0101 | D | 1101
6 | 0110 | E | 1110
7 | 0111 | F | 1111
10AF16 = ?2
1 0 A F
1111
1010
0000
10AF16 =
10000101011112
0001

## Slide 26: Binary to Hexa-Decimal
Technique
  From given fractional point, group bits in fours to right and group bits in fours to left
  If, left with less than 4 bits at the end then stuff 0s to make it group of four
  Convert to hexadecimal digits
Example
101101.01112 = ?16
0010
101101.01112 =
2D.716
0111
1101
2
D
7
.

## Slide 27: Octal to Hexa-Decimal
Technique
  Convert Octal to Binary
  From given fractional point, group bits in fours to right and group bits in fours to left
  Convert Binary to Hexa-Decimal
Example
10768 = ?16
1 0 7 6
110
111
000
10768 =
23E16
001
1110
0011
0010
E
3
2

## Slide 28: Hexa-Decimal to Octal
Technique
  Convert Hexa-Decimal to Binary
  From given fractional point, group bits in threes to right and group bits in threes to left
  Convert Binary to Octal
Example
1F0C16 = ?8
1 F 0 C
1100
0000
1111
1F0C16 =
174148
0001
100
001
100
4
1
4
111
7
001
1
000
0

## Slide 29: Signed Binary Numbers
Two ways of representing signed numbers:
  1) Sign-magnitude form, 2) Complement form.
Most of computers use complement form for negative number notation.
1’s complement and 2’s complement are two different methods in this type.

## Slide 30: 1’s Complement
1’s complement of a binary number is obtained by subtracting each digit of that binary number from 1.
Example
1
1
1
1
1
1
0
1
0
0
1
0
-
(1’s complement of 1101)
1
1
1
.
1
0
1
.
0
1
0
.
-
(1’s complement of 101.01)
1
1
0
1
1
0
Shortcut: Invert the numbers from 0 to 1 and 1 to 0

## Slide 31: 2’s Complement
2’s complement of a binary number is obtained by adding 1 to its 1’s complement.
Example
1
1
1
1
1
1
0
0
0
0
1
1
-
(2’s complement of 1100)
0
1
0
.
-
(2’s complement of 101.01)
1
1
1
.
1
1
1
0
1
.
0
1
1
0
1
0
1
0
0
1
+
+
0
1
0
1
1
.
Shortcut: Starting from right side, all bits are same till first 1 occurs and then invert rest of the bits

## Slide 32: Representation of negative number in 2’s complement form
Express -65.5 in 12 bit 2’s complement form.
2
65
1
2
32
0
2
16
0
2
8
0
2
4
0
2
2
0
2
1
1
0
0.5 x 2 =
1.0
65.510 =
01000001.10002
So, result in 12-bit binary is as follows:
For negative number, we have to convert this into 2’s complement form
-65.510 =
10111110.10002

## Slide 33: Accuracy in Binary Number Conversion
Example
Convert (0.252)10 to binary with an error less than 1%.
Solution
Absolute value of allowable error is found by calculating 1% of the number
Maximum error due to truncation is set to be less than allowable error by solving from . This equation is written as
Inverting both sides of the inequality

## Slide 34: Accuracy in Binary Number Conversion
Taking log of both sides and solving for
This indicates that the use of 9 bits in the binary number will guarantee an error less than 1%.
So the conversion is carried out to 9 places which results in

## Slide 35: Binary arithmetic operations
Section - 3

## Slide 36: Binary Addition & Subtraction
Rules for binary addition
Rules for binary subtraction
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10 i.e. 0 with a carry of 1
1
1
0
1
0
1
1
1
0
1
0
1
1
1
1
1
1
+
.
1
0
1
.
0
1
1
.
0
0
0
1
1
0 – 0 = 0
1 – 1 = 0
1 – 0 = 1
0 – 1 = 1, with a borrow 1
1
0
1
0
0
1
1
1
0
0
1
0
-
.
0
1
0
.
1
1
1
.
0
1
1
1
0
1
1
1
0
1
1
0

## Slide 37: Binary Multiplication & Division
Multiplication
Division
1 0 1 1 1
1 0 0 1 1
x
1
1
1
0
1
1
1
1
0
1
0
0
0
0
0
0
0
0
0
0
1
1
1
0
1
1
0
1
0
1
1
0
1
1
1 0 1 1 0 1
110
0
0 0 0
1 0 1
1
1 1 0
1 0 1
0
1 1 0
1 0 0
1
1 1 0
1 1
1
1
1
.
1
0
1 1 0
0 0 0

## Slide 38: Complements arithmetic
Section - 4

## Slide 39: 9’s Complement
9’s complement of a decimal number is obtained by subtracting each digit of that decimal number from 9.
Example
9
9
9
9
3
4
6
5
6
5
3
4
-
(9’s complement of 3465)
9
9
9
.
7
8
2
.
2
1
7
.
-
(9’s complement of 782.54)
9
9
5
4
4
5

## Slide 40: 10’s Complement
10’s complement of a decimal number is obtained by adding 1 to its 9’s complement.
Example
9
9
9
9
3
4
6
5
6
5
3
4
-
(10’s complement of 3465)
2
1
7
.
-
(10’s complement of 782.54)
9
9
9
.
9
9
7
8
2
.
5
4
4
5
1
6
5
3
5
1
+
+
2
1
7
4
6
.

## Slide 41: Subtraction using 9’s complement & 10’s complement
Using 9’s complement
  Obtain 9’s complement of subtrahend
  Add the result to minuend and call it intermediate result
  If carry is generated then answer is positive and add the carry to Least Significant Digit (LSD)
  If there is no carry then answer is negative and take 9’s complement of intermediate result and place negative sign to the result.
Using 10’s complement
  Obtain 10’s complement of subtrahend
  Add the result to minuend
  If carry is generated then answer is positive, ignore carry and result itself is answer
  If there is no carry then answer is negative and take 10’s complement of intermediate result and place negative sign to the result.

## Slide 42: Subtraction using 9’s complement (Examples)
Example - 1
745.81 – 436.62
7
4
5
.
4
3
6
.
-
8
1
6
2
7
4
5
.
8
1
5
6
3
.
+
3
7
3
0
9
.
1
1
8
+
1
3
0
9
.
1
9
3
0
9
.
1
9
9’s complement

## Slide 43: Subtraction using 9’s complement (Examples)
Example - 2
7
4
5
.
4
3
6
.
-
8
1
6
2
436.62 - 745.81
2
5
4
.
+
1
8
6
9
0
.
8
0
3
0
9
.
1
9
3
0
9
.
1
9
-
4
3
6
.
6
2
-
9’s complement
9’s complement
As carry is not generated, so take 9’s complement of the intermediate result and add ‘ – ‘ sign to the result

## Slide 44: Subtraction using 10’s complement (Examples)
Example - 1
7
4
5
.
4
3
6
.
-
8
1
6
2
745.81 – 436.62
5
6
3
.
+
7
4
5
.
8
1
3
8
3
0
9
.
1
1
9
3
0
9
.
1
9
Ignore the carry
10’s complement

## Slide 45: Subtraction using 10’s complement (Examples)
Example - 2
7
4
5
.
4
3
6
.
-
8
1
6
2
436.62 - 745.81
2
5
4
.
+
1
9
6
9
0
.
8
1
3
0
9
.
1
9
3
0
9
.
1
9
-
4
3
6
.
6
2
-
10’s complement
10’s complement
As carry is not generated, so take 10’s complement of the intermediate result and add ‘ – ‘ sign to the result

## Slide 46: Subtraction using 1’s complement & 2’s complement
Using 1’s complement
  Obtain 1’s complement of subtrahend
  Add the result to minuend and call it intermediate result
  If carry is generated then answer is positive and add the carry to Least Significant Bit (LSB)
  If there is no carry then answer is negative and take 1’s complement of intermediate result and place negative sign to the result.
Using 2’s complement
  Obtain 2’s complement of subtrahend
  Add the result to minuend
  If carry is generated then answer is positive, ignore carry and result itself is answer
  If there is no carry then answer is negative and take 2’s complement of intermediate result and place negative sign to the result.

## Slide 47: Subtraction using 1’s complement (Examples)
Example - 1
6
8
.
2
7
.
-
7
5
5
0
68.75 - 27.50
+
4
1
.
2
5
1’s complement
0
0
0
.
1
1
1
0
0
0
1
0
0
+
1
0
0
.
1
0
0
1
1
0
1
1
1
+
1
0
0
1
.
1
0
0
0
1
0
0
1
1
1
0
1
0
.
0
1
0
0
1
0
1
0
0

## Slide 48: Subtraction using 1’s complement (Examples)
Example - 2
43.25 - 89.75
As carry is not generated, so take 1’s complement of the intermediate result and add ‘ – ‘ sign to the result
4
3
.
8
9
.
-
2
5
7
5
-
4
6
.
5
0
1’s complement
1
0
1
.
0
1
0
1
1
0
0
0
0
+
1
0
0
.
1
1
0
1
0
0
0
1
1
0
0
1
.
0
0
1
1
0
1
1
1
1
1
1
0
.
1
1
0
0
1
0
0
0
0
1’s complement

## Slide 49: Subtraction using 2’s complement (Examples)
Example - 1
6
8
.
2
7
.
-
7
5
5
0
68.75 – 27.50
+
4
1
.
2
5
2’s complement
0
0
0
.
1
1
1
0
0
0
1
0
0
+
1
0
0
.
1
0
0
1
1
1
0
0
0
0
0
1
.
1
0
1
0
1
0
0
1
0
0
0
0
1
.
1
0
1
0
1
0
0
0
0
Ignore Carry bit

## Slide 50: Subtraction using 2’s complement (Examples)
Example - 2
43.25 - 89.75
As carry is not generated, so take 2’s complement of the intermediate result and add ‘ – ‘ sign to the result
4
3
.
8
9
.
-
2
5
7
5
-
4
6
.
5
0
2’s complement
1
0
1
.
0
1
0
1
1
0
0
0
0
+
1
0
0
.
1
1
0
1
0
0
1
0
0
0
0
1
.
0
1
0
1
0
1
1
0
0
1
1
0
.
1
1
0
0
1
0
0
0
0
2’s complement

## Slide 51: Binary Codes
Section - 5

## Slide 52: 8421 BCD Code (Natural BCD Code)
Each decimal digit, 0 through 9, is coded by 4-bit binary number
8, 4, 2 and 1 weights are attached to each bit
BCD code is weighted code
1010, 1011, 1100, 1101, 1110 and 1111 are illegal codes
Less efficient than pure binary
Arithmetic operations are more complex than in pure binary
Example
1 4
0100
0001
Decimal
BCD
Binary
1110

## Slide 53: Binary Codes
Decimal | Binary | BCD
0 | 0 | 0000
1 | 1 | 0001
2 | 10 | 0010
3 | 11 | 0011
4 | 100 | 0100
5 | 101 | 0101
6 | 110 | 0110
7 | 111 | 0111
Decimal | Binary | BCD
8 | 1000 | 1000
9 | 1001 | 1001
10 | 1010 | 0001 0000
11 | 1011 | 0001 0001
12 | 1100 | 0001 0010
13 | 1101 | 0001 0011
14 | 1110 | 0001 0100
15 | 1111 | 0001 0101

## Slide 54: BCD Addition
Example - 1
0
0
1
0
0
0
0
1
0
0
1
1
+
0
1
0
1
0
0
1
1
1
0
0
0
2
5
1
3
+
3
8
No carry, no illegal code. So, this is the correct sum.
1
1
1
Rule: If there is an illegal code or carry is generated as a result of addition, then add 0110 to particular that 4 bits of result.

## Slide 55: BCD Addition
Example - 2
0110
0111
1001
+
.0110
679.6
536.8
+
1216.4
All are illegal codes
0101
0011
0110
.1000
1011
1010
1111
.1110
+0110
+0110
+0110
+.0110
10001
10000
10101
1.0100
1
+
1
+
1
+
1
+
0010
0001
0110
.0100
0001
Add 0110 to each
Propagate carry
Corrected sum
1
1
1
1

## Slide 56: BCD Subtraction
Example - 1
0
0
1
1
0
0
0
1
0
0
1
0
-
1
0
0
0
0
1
0
1
0
0
1
1
3
8
1
5
-
2
3
No borrow. So, this is the correct difference.
Rule: If one 4-bit group needs to take borrow from neighbor, then subtract 0110 from the group which is receiving borrow.

## Slide 57: BCD Subtraction
Example - 2
0010
0000
0110
-
.0111
206.7
147.8
-
58.9
Borrows are present
0001
0100
0111
.1000
0000
1011
1110
.1111
-0110
-0110
-.0110
0101
1000
.1001
Subtract 0110
Corrected difference

## Slide 58: Excess Three (XS-3) Code
Excess Three Code = 8421 BCD + 0011(3)
XS-3 code is non-weighted BCD code
Also known as self complementing code
0000, 0001, 0010, 1101, 1110 and 1111 are illegal codes
Example
1 4
0100
0001
Decimal
BCD
XS-3
0100
0111

## Slide 59: XS-3 Addition
Example
0101
0111
1010
+
.1001
247.6
359.4
+
607.0
Carry generated
0110
1000
1100
.0111
1011
1111
10110
1.0000
- 0011
+0011
+0011
+.0011
1011
10000
0111
.0000
1
+
1
+
1
+
Propagate carry
.0000
0111
0000
1100
Rule: Add 0011 to groups which generate carry and Subtract 0011 from groups which do not generate carry
Corrected Sum in XS-3
.0011
1010
0011
1001

## Slide 60: XS-3 Subtraction
Example
1000
1010
.1001
-
57.6
27.8
-
29.8
0101
1010
.1011
0010
1111
.1110
-0011
+0011
0101
1100
.1011
Rule: Subtract 0011 from groups which generate borrow and Add 0011 to groups which do not generate borrow
-.0011

## Slide 61: Gray Code
Only one bit changes between each pair of successive code words (Unit distance code).
Gray code is a reflected code.
Gray codes are designed recursively using following rules:
  1-bit Gray code has two code words, 0 and 1.
  The first 2n code words of an (n+1)-bit Gray code equal the code words of n-bit gray code, written in order with a leading 0 appended.
  The last 2n code words of an (n+1)-bit Gray code equal the code words of n-bit gray code, but written in reverse order with a leading 1 appended.

## Slide 62
Gray Code |  |  |  | Decimal | 4-bit Binary
1-bit | 2-bit | 3-bit | 4-bit |  | 
0 | 0 0 | 0 0 0 | 0 0 0 0 | 0 | 0000
1 | 0 1 | 0 0 1 | 0 0 0 1 | 1 | 0001
 | 1 1 | 0 1 1 | 0 0 1 1 | 2 | 0010
 | 1 0 | 0 1 0 | 0 0 1 0 | 3 | 0011
 |  | 1 1 0 | 0 1 1 0 | 4 | 0100
 |  | 1 1 1 | 0 1 1 1 | 5 | 0101
 |  | 1 0 1 | 0 1 0 1 | 6 | 0110
 |  | 1 0 0 | 0 1 0 0 | 7 | 0111
 |  |  | 1 1 0 0 | 8 | 1000
 |  |  | 1 1 0 1 | 9 | 1001
 |  |  | 1 1 1 1 | 10 | 1010
 |  |  | 1 1 1 0 | 11 | 1011
 |  |  | 1 0 1 0 | 12 | 1100
 |  |  | 1 0 1 1 | 13 | 1101
 |  |  | 1 0 0 1 | 14 | 1110
 |  |  | 1 0 0 0 | 15 | 1111

## Slide 63: Binary to Gray and Gray to Binary Conversion
Conversion of n-bit Binary number (B) to Gray Code (G) is as follows:
Example: Convert (1001)2 to Gray Code.
1
Binary
Gray
0
0
1
1
1
0
1

## Slide 64: Gray to Binary Conversion
Conversion of n-bit Gray Code (G) to Binary Number (B) is as follows:
Example: Convert Gray code 1101 to Binary.
1
Gray
Binary
1
0
1
1
0
0
1

## Slide 65: Error-Detecting Codes
Noise can alter or distort the data in transmission.
The 1s may get changed to 0s and 0s to 1s.
Because digital systems must be accurate to the digit, errors can pose a serious problem.
Single bit error should be detect & correct by different schemes.
Parity, Check Sums and Block Parity are few examples of error detecting code.

## Slide 66: Parity
Parity bit is the simplest technique.
There are two types of parity – Odd parity and Even parity.
For odd parity, the parity is set to a 0 or a 1 at the transmitter such that the total number of 1 bits in the word including the parity bit is an odd number.
For even parity, the parity is set to a 0 or a 1 at the transmitter such that the total number of 1 bits in the word including the parity bit is an even number.
For example, 0110 binary number has “1” as Odd parity and “0” as Even parity.
Detect a single-bit error but can not detect two or more errors within the same word.
In any practical system, there is always a finite probability of the occurrence of single error.
E.g. In an even-parity scheme, code 10111001 is erroneous because number of 1s is odd(5), while code 11110110 is error free because number of 1s is even(6).

## Slide 67: Block Parity
01011011
10010101
01101110
11010011
10001101
01110111
0
1
0
0
1
1
0
01110110
Parity Column
01011011
10010101
01100110
11010011
10001101
01110111
0
1
0
0
1
1
0
01110110
01011011
10010101
01101110
10000011
10001101
01110111
0
1
0
0
1
1
0
01110110
Parity Row

## Slide 68: Error Correcting Code
7-bit Hamming Code is widely used error correcting code, containing 4 bits of data and 3 bits of even parity.
Pattern: P1 P2 D3 P4 D5 D6 D7
Group - 1: P1D3D5D7
Group - 2: P2D3D6D7
Group - 3: P4D5D6D7
Example: Data = 1101
P1 P2 D3 P4 D5 D6 D7 = P1 P2 1 P4 1 0 1
P1 D3 D5 D7 = 1 1 1 1
P2 D3 D6 D7 = 0 1 0 1
P4 D5 D6 D7 = 0 1 0 1
7-bit Hamming Code is 1 0 1 0 1 0 1
How to detect error?
Example: Received data = 1001001
P1 P2 D3 P4 D5 D6 D7 = 1 0 0 1 0 0 1
P1 D3 D5 D7 = 1 0 0 1 (No Error)
P2 D3 D6 D7 = 0 0 0 1 (Error)
P4 D5 D6 D7 = 1 0 0 1 (No Error)
The error word is 0 1 0 = 210.
Complement the 2nd bit (from left).
Correct code is 1 1 0 1 0 0 1