## Slide 1: Unit-2 Simplification of Logic function
krunal.vyas@darshan.ac.in
9601901005
Computer Science & Engineering
Prof. Krunal D Vyas
Digital Fundamentals (DF)
DU #2101CS303

## Slide 2

Looping
Outline
  Standard representation of logic function: SOP and POS
  Boolean algebra laws - De Morgan’s theorem
  K-map representation
  Simplification using K-map
  K-map with Don’t care conditions
  Variable Entered Map (VEM) method
  Tabulation (Q-M) method of function realization
  Realize logic function using gates

## Slide 3: Standard representation of logic function: SOP and POS
Section - 1

## Slide 4: Boolean functions & representation
Sum-of-products (SOP) form (Disjunctive Normal Form)
Products-of-sums (POS) form (Conjunctive Normal Form)

## Slide 5: Boolean functions & representation
Standard sum-of-products form (Minterm)
Contains all the variables of the function either in complemented or uncomplemented form.
Variable appears in uncomplemented form if it has a value of 1 in the combination and appears in complemented form if it has a value of 0 in the combination
Sum of minterms whose value is equal to 1 is the standard sum of products form of the function.
Minterms are denoted as m0, m1, m2, …,
For 3 variable function, m0=, m1=, m2=, m3=, m4=, m5=, m6=, and m7=
Value of Minterm = 1

## Slide 6: Boolean functions & representation
Canonical SOP form is shown by the sum of minterms for which the function equals 1.
f(A,B,C) = m1 + m2 + m3 + m5
Or
f(A,B,C) =
Standard product-of-sum form (Maxterm)
Derived by considering the combinations of which f = 0
Each term is a sum of all the variables
Variable appears in uncomplemented form if it has a value of 0 in the combination and appears in complemented form if it has a value of 1 in the combination

## Slide 7: Boolean functions & representation
A sum term which contains each of the n variables in either complemented or uncomplemented form is called a maxterm.
Maxterms are denoted as M0, M1, M2, …,
f(A,B,C) = M0M1M6M7
Or
f(A,B,C) =
Value of Maxterm = 0

## Slide 8: Boolean algebra laws - De Morgan’s theorem
Section - 2

## Slide 9: Boolean Algebra Laws
AND laws
Commutative laws
OR laws
Associative laws

## Slide 10: Boolean Algebra Laws
Distributive laws
Idempotent laws
Redundant Literal Rule
Absorption laws
De Morgan’s Theorem
Break the line change the sign

## Slide 11: Proof of
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
C
0
1
0
1
0
1
0
1
A+B+C
0
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
From truth table, it is clearly visible that L.H.S. = R.H.S. Hence, the complement of a sum of variables is equal to the product of their individual complements.
L.H.S.
R.H.S.

## Slide 12: Proof of
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
C
0
1
0
1
0
1
0
1
A B C
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
0
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
0
From truth table, it is clearly visible that L.H.S. = R.H.S. Hence, the complement of a product of variables is equal to the sum of their individual complements.
L.H.S.
R.H.S.

## Slide 13: Reducing Boolean Expression (Example – 1)
Reduce the expression
(Distributive law)
(Distributive law)
(A.A = A)
(1 + A = 1)

## Slide 14: Reducing Boolean Expression (Example – 2)
Reduce the expression
(De-Morgan’s law)
(De-Morgan’s law)
(Distributive law)
(Distributive law)
(A.A’ = 0)
(Distributive law)
(A.A’ = 0)

## Slide 15: Exercise

## Slide 16: K-map representation
Section - 3

## Slide 17: Introduction to K-Maps
Simplification of Boolean functions leads to simpler (and usually faster) digital circuits.
Simplifying Boolean functions using identities is time-consuming and error-prone.
This special section presents an easy, systematic method for reducing Boolean expressions.
A K-Map is a matrix consisting of rows and columns that represent the output values of a Boolean function.
The output values placed in each cell are derived from the minterms of a Boolean function.
A minterm is a product term that contains all of the function’s variables exactly once, either complemented or not complemented.

## Slide 18: 2 – Variable K-Map
The two variables A and B have four possible combinations that can be represented by the map as follows
A
B
0
1
0
1
0
1
2
3
A | B | Minterm
0 | 0 | m0 = A’B’
0 | 1 | m1 = A’B
1 | 0 | m2 = AB’
1 | 1 | m3 = AB

## Slide 19: 3 – Variable K-Map
The three variables A, B and C have eight possible combinations that can be represented by the map as follows
AB
C
00
10
0
1
0
1
2
3
A | B | C | Minterm
0 | 0 | 0 | m0 = A’B’C’
0 | 0 | 1 | m1 = A’B’C
0 | 1 | 0 | m2 = A’BC’
0 | 1 | 1 | m3 = A’BC
1 | 0 | 0 | m4 = AB’C’
1 | 0 | 1 | m5 = AB’C
1 | 1 | 0 | m6 = ABC’
1 | 1 | 1 | m7 = ABC
01
11
4
5
6
7
Minterm Number

## Slide 20: 4 – Variable K-Map
The four variables A, B, C and D have sixteen possible combinations that can be represented by the map as follows
A | B | C | D | Minterm
0 | 0 | 0 | 0 | m0 = A’B’C’D’
0 | 0 | 0 | 1 | m1 = A’B’C’D
0 | 0 | 1 | 0 | m2 = A’B’CD’
0 | 0 | 1 | 1 | m3 = A’B’CD
0 | 1 | 0 | 0 | m4 = A’BC’D’
0 | 1 | 0 | 1 | m5 = A’BC’D
0 | 1 | 1 | 0 | m6 = A’BCD’
0 | 1 | 1 | 1 | m7 = A’BCD
A | B | C | D | Minterm
1 | 0 | 0 | 0 | m8 = AB’C’D’
1 | 0 | 0 | 1 | m9 = AB’C’D
1 | 0 | 1 | 0 | m10 = AB’CD’
1 | 0 | 1 | 1 | m11 = AB’CD
1 | 1 | 0 | 0 | m12 = ABC’D’
1 | 1 | 0 | 1 | m13 = ABC’D
1 | 1 | 1 | 0 | m14 = ABCD’
1 | 1 | 1 | 1 | m15 = ABCD
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11

## Slide 21: Simplification using K-map
Section - 4

## Slide 22: Reduce Boolean Expression
Consider the function:
Its K-Map is given below.
What is the largest group of 1’s that is a power of 2?
This grouping tells us that changes in the variables A and B have no influence upon the value of the function: They are irrelevant.
AB
C
00
10
0
1
0
1
2
3
01
11
4
5
6
7
1
1
1
1

## Slide 23: Examples (SOP)
1
1
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
1
AB
C
00
10
0
1
01
11
0
1
2
3
4
5
6
7

## Slide 24: Examples (SOP)
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
1
1
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1

## Slide 25: Example (POS)
f(A,B,C,D) =
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
0
0
0
0
0
0
0
0

## Slide 26: K-map with Don’t care conditions
Section - 5

## Slide 27: Don’t care conditions
Suppose we are given a problem of implementing a circuit to generate a logical 1 when a 2, 7, or 15 appears on a four-variable input.
A logical 0 should be generated when 0, 1, 4, 5, 6, 9, 10, 13 or 14 appears.
The input conditions for the numbers 3, 8, 11 and 12 never occur in the system. This means we don’t care whether inputs generate logical 1 or logical 0.
Don’t care combinations are denoted by ‘x’ in K-Map which can be used for the making groups.
The above example can be represented as
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
x
x
f(A,B,C,D) = + d(3,8,11,12)
x
x

## Slide 28: Example (Don’t care)
WX
YZ
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
F(W,X,Y,Z) = + d(0,2,5)
x
x
1
1
x

## Slide 29: Variable Entered Map (VEM) method
Section - 6

## Slide 30: Variable-Entered Map (VEM)
Variable-entered map can be used to plot an n-variable problem on n – 1 variable map
Possible to reduce the map dimension by two or three in some cases
Advantage of using VEM occurs in design problems involving multiplexers
Map-entered variable for 3 variable function
Consider the function
Considering value of to be function of map location with the variable and plotting 2 variable map.
A
B
0
1
0
1
X=1 if C’=1
X=1 if C’=1
X=1 if C’=1 or if C = 1
X=0
A
B
0
1
0
1
C’
C’
0
C + C’

## Slide 31: Reducing Expressions with VEM (Example)
Choose groups of similar terms to cover all nonzero terms appearing in the map except “don’t care” terms.
Rest complete process is similar to K-Map
AB
C
00
10
0
1
01
11
D+D’
D
D
D
D

## Slide 32: Reducing Expressions with VEM (Example)
AB
C
00
10
0
1
01
11
D+D’
D
D’
D’
D+D’
D’
D’

## Slide 33: Reducing Expressions with VEM (Example)
f
AB
CD
00
10
00
01
01
11
11
10
E
E
E’
E’
E+E’
E+E’
E+E’
E’

## Slide 34: Tabulation (Q-M) method of function realization
Section - 7

## Slide 35: Tabulation Method (Quine-McCluskey Method)
Fundamental idea for tabulation method is combining theorem.
The above theorem is applied repeatedly to all adjacent pairs of terms which results in prime implicants.
Consider the minimization of the expression
= A’B’C’ + A’B’C + AB’C’ + AB’C
= A’B’(C + C’) + AB’(C + C’)
= A’B’ + AB’
= B’(A + A’)
= B’

## Slide 36: Procedure for minimization using Tabulation Method
List all the minterms.
Arrange all minterms in groups of the same number of 1s in their binary representation in column 1. Start with the least number of 1s group and continue with groups of increasing number of 1s.
Compare each term of the lowest index group with every term in the succeeding group. Whenever possible, combine the two terms being compared by means of the combining theorem. Two terms from adjacent groups are combinable, if their binary representations differ by just a single digit in the same position; the combined terms consist of the original fixed representation with the differing one replaced by a dash (-). Place a check mark (√) next to every term, which has been combined with at least one term and write the combined terms in column 2. Repeat this by comparing each term in a group of index i with every term in the group of index i + 1, until all possible applications of the combining theorem have been exhausted.

## Slide 37: Procedure for minimization using Tabulation Method
Compare the terms generated in step 3 in the same fashion; combine two terms which differ by only a single 1 and whose dashes are in the same position to generate a new term. Two terms with dashes in different positions cannot be combined. Write the new terms in column 3 and put a check mark next to each term which has been combined in column 2. Continue the process with terms in columns 3, 4 etc. until no further combinations are possible. The remaining unchecked terms constitute the set of prime implicants of the expression.
List all the prime implicants and draw the prime implicant chart. (The don’t cares if any should not appear in the prime implicant chart).
Obtain the essential prime implicants and write the minimal expression.

## Slide 38: Tabulation Method (Example)
Step – 1: List all minterms
Minterms | Binary Designation
0 | 0 0 0 0
1 | 0 0 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
13 | 1 1 0 1
14 | 1 1 1 0
15 | 1 1 1 1
Step – 2: Arrange all minterms in groups of same number of 1s
Column 1 |  | 
Index | Minterms | Binary Designation
Index 0 | 0 | 0 0 0 0
Index 1 | 1 8 | 0 0 0 1 1 0 0 0
Index 2 | 6 9 | 0 1 1 0 1 0 0 1
Index 3 | 7 13 14 | 0 1 1 1 1 1 0 1 1 1 1 0
Index 4 | 15 | 1 1 1 1

## Slide 39: Tabulation Method (Example) Cont..
Step – 3: Compare each term of the lowest index group with every term in the succeeding group till no change
Column 2 | 
Pairs | A B C D
0, 1 0, 8 | 0 0 0 _ _ 0 0 0
1, 9 8, 9 | _ 0 0 1 1 0 0 _
6, 7 6, 14 9, 13 | 0 1 1 _ _ 1 1 0 1 _ 0 1
7, 15 13, 15 14, 15 | _ 1 1 1 1 1 _ 1 1 1 1 _
Column 1 |  | 
Index | Minterms | Binary Designation
Index 0 | 0 | 0 0 0 0
Index 1 | 1 8 | 0 0 0 1 1 0 0 0
Index 2 | 6 9 | 0 1 1 0 1 0 0 1
Index 3 | 7 13 14 | 0 1 1 1 1 1 0 1 1 1 1 0
Index 4 | 15 | 1 1 1 1
√
√
√
√
√
√
√
√
√

## Slide 40: Tabulation Method (Example) Cont..
Pairs | A B C D
0, 1 0, 8 | 0 0 0 _ _ 0 0 0
1, 9 8, 9 | _ 0 0 1 1 0 0 _
6, 7 6, 14 9,13 | 0 1 1 _ _ 1 1 0 1 _ 0 1
7, 15 13, 15 14, 15 | _ 1 1 1 1 1 _ 1 1 1 1 _
Step – 4: Compare the terms generated in step 3 in the same fashion until no further combinations are possible
Quads | A B C D
0, 1, 8, 9 | _ 0 0 _
6, 7, 14, 15 | _ 1 1 _
√
√
√
√
√
√
√
√
P
Q
R
S

## Slide 41: Tabulation Method (Example) Cont..
Step – 5: List all prime implicants and draw prime implicants chart
Prime Implicants : P(BC), Q(B’C’), R(ABD), S(AC’D)
 | √ | √ | √ | √ | √ | √ |  | √ | √
PIs | 0 | 1 | 6 | 7 | 8 | 9 | 13 | 14 | 15
P (6,7,14,15) |  |  | x | x |  |  |  | x | x
Q (0,1,8,9) | x | x |  |  | x | x |  |  | 
R (13,15) |  |  |  |  |  |  | x |  | x
S (9,13) |  |  |  |  |  | x | x |  | 
Step – 6: Obtain essential prime implicants and minimal expression
Essential Prime Implicants : P(BC)
, Q(B’C’)
Minimal expression : P + Q + R = BC + B’C’ + ABD
OR P + Q + S = BC + B’C’ + AC’D
As minterm 13 is covered by R and S

## Slide 42: Realize logic function using gates
Section - 8

## Slide 43: Realizing Logic Function with Gates
Implement AB’ + C’D using AND, OR & Invert Gates
A
B
C
D

## Slide 44: Converting AND/OR/Invert Logic to NAND/NOR Logic
Draw the circuit in AOI logic.
If NAND hardware is chosen, add a circle at the output of each AND gate and at the inputs to all the OR gates.
If NOR hardware is chosen, add a circle at the output of each OR gate and at the inputs to all the AND gates.
Add or subtract an inverter on each line that received a circle in steps 2 or 3 so that the polarity of signals on those lines remains unchanged from that of the original diagram.
Replace bubbled OR by NAND and bubbled AND by NOR.
Eliminate double inversions.

## Slide 45: Converting AND/OR/Invert Logic to NAND/NOR Logic (Example)
Implement the following AOI logic using NAND logic
Put a circle at the output of each AND gate and at the inputs to all OR gates

## Slide 46: Converting AND/OR/Invert Logic to NAND/NOR Logic (Example)
Add an inverter to each of the lines that received only one circle at input so that polarity remains unchanged.

## Slide 47: Converting AND/OR/Invert Logic to NAND/NOR Logic (Example)
Replace bubbled OR gates and NOT gates by NAND gates.