## Slide 1: Unit-4 Sequential Digital Circuits
krunal.vyas@darshan.ac.in
9601901005
Computer Science & Engineering
Prof. Krunal D Vyas
Digital Fundamentals (DF)
DU #2101CS303

## Slide 2

Looping
Outline
  SR Latch, Flip-flop: SR, D, JK, T
  Shift register
  Asynchronous Counter: Ripple up/down counters, Modulo counters
  Synchronous Counter
  Sequential Generator: Direct and Indirect

## Slide 3: SR Latch, Flip-flop: SR, D, JK, T
Section - 1

## Slide 4: Sequential Switching Circuits
Sequential switching circuits are circuits whose output levels at any instant of time are dependent on the levels present at the inputs at that time and on the state of the circuit, i.e., on the prior input level conditions (i.e. on its past inputs)
The past history is provided by feedback from the output back to the input.
Made up of combinational circuits and memory elements.
Eg. Counters, shift registers, serial adder, etc.
Combinational Circuit
Memory elements
Inputs
Outputs

## Slide 5: Sequential Circuits v/s Combinational Circuits
Sequential Circuits | Combinational Circuits
In sequential circuits, the output variables at any instant of time are dependent on the present input variables and on the present state, i.e., on the past history of the system. | In combinational circuits, the output variables at any instant of time are dependent only on the present input variables.
Memory unit is required to store the past history of the input variables in sequential circuits. | Memory unit is not required in combinational circuits.
Sequential circuits are slower than combinational circuits. | Combinational circuits are faster because the delay between the input and the output is due to propagation delay of gates only.
Sequential circuits are comparatively harder to design. | Combinational circuits are easy to design.

## Slide 6: Flip-flop & Latch
A flip-flop, known formally as bi-stable multivibrator, has two stable states.
It can remain in either of the states indefinitely.
Its state can be changed by applying the proper triggering signal.
Latch is used for certain flip-flop which are non-clocked.
These flip-flops ‘latch on’ to a 1 or a 0 immediately upon receiving the input pulse called SET or RESET.

## Slide 7: S-R Latch
The simplest type of flip-flop is called an S-R latch.
It has two outputs labelled Q and Q’ and two inputs labelled S and R. The state of the latch corresponds to the level of Q (HIGH or LOW, 1 or 0) and Q’ is the complement of that state.
It can be constructed using either two cross-coupled NAND gates or two cross-coupled NOR gates.
Using two NOR gates, an active-HIGH S-R latch can be constructed and using two NAND gates an active-LOW S-R latch can be constructed.
The name of the latch, S-R or SET-RESET, is derived from the names of its inputs.

## Slide 8: NOR Gate S-R latch (Active High)
S
R
Q
Q’
Inputs
Outputs
S | R | Qn | Qn+1 | State
0 0 | 0 0 | 0 1 | 0 1 | No Change
0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 0 1 | x x | Indeterminate (invalid)
R
S
Q
Q’
Logic diagram
Logic Symbol
1
0
0
0
0
0
1

## Slide 9: NAND Gate S-R latch (Active Low)
S | R | Qn | Qn+1 | State
0 0 | 0 0 | 0 1 | x x | Indeterminate (invalid)
0 0 | 1 1 | 0 1 | 1 1 | Set
1 1 | 0 0 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 1 | 0 1 | No Change
S
R
Q
Q’
Logic diagram
1
0
0
0
1
1

## Slide 10: Gated S-R Latch (S-R Flip-flop)
S
R
Q
Q’
EN | S | R | Qn | Qn+1 | State
1 1 | 0 0 | 0 0 | 0 1 | 0 1 | No Change
1 1 | 0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 1 1 | 0 1 | x x | Indeterminate (invalid)
0 0 | x x | x x | 0 1 | 0 1 | No Change
S
R
Q
Q’
Logic diagram
Logic Symbol
EN
EN
0
1
1
1
1
1
0
0
0
1
1
1

## Slide 11: Gated D-Latch (D Flip-flop)
D
Q
Q’
EN | D | Qn | Qn+1 | State
1 1 | 0 0 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 1 | 1 1 | Set
0 0 | x x | 0 1 | 0 1 | No Change
D
Q
Q’
Logic diagram
Logic Symbol
EN
EN
1
1
1
1
0
0
0
1
0
1
1
0
0

## Slide 12: J-K Flip-flop
J
K
Q
Q’
Logic Symbol
EN
J
K
Q
Q’
EN
EN | J | K | Qn | Qn+1 | State
1 1 | 0 0 | 0 0 | 0 1 | 0 1 | No Change
1 1 | 0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 1 1 | 0 1 | 1 0 | Toggle
0 0 | x x | x x | 0 1 | 0 1 | No Change
Logic diagram
1
0
1
0
0
0
1
1
1
1
0
1

## Slide 13: T Flip-flop
T
Q
Q’
Logic Symbol
EN
T
Q
EN
Q’
EN | T | Qn | Qn+1 | State
1 1 | 0 0 | 0 1 | 0 1 | No change
1 1 | 1 1 | 0 1 | 1 0 | Toggle
0 0 | x x | 0 1 | 0 1 | No Change
Logic diagram

## Slide 14: Shift register
Section - 2

## Slide 15: Registers
As a flip-flop (FF) can store only one bit of data, a 0 or a 1, it is referred to as a single-bit register.
A register is a set of FFs used to store binary data.
The storage capacity of a register is the number of bits (1s and 0s) of digital data it can retain.
Loading a register means setting or resetting the individual FFs, i.e. inputting data into the register so that their states correspond to the bits of data to be stored.
Loading may be serial or parallel.
In serial loading, data is transferred into the register in serial form i.e. one bit at a time.
In parallel loading, the data is transferred into the register in parallel form meaning that all the FFs are triggered into their new states at the same time.
Types of registers are:
  Buffer register, Shift register, Bidirectional shift register, Universal shift register

## Slide 16: Shift Register
A number of FFs connected together such that data may be shifted into and shifted out of them is called a shift register.
Data may be shifted into or out of the register either in serial form or in parallel form.
So, there are four basic types of shift registers:
  serial-in, serial-out
  serial-in, parallel-out
  parallel-in, serial-out
  parallel-in, parallel-out
Data may be rotated left or right. Data may be shifted from left to right or right to left at will, i.e. in a bidirectional way.
Also, data may be shifted in serially (in either way) or in parallel and shifted out serially (in either way) or in parallel.

## Slide 17: Data transmission in shift register
Serial-in, serial-out shift-right, shift register
Serial data input
Serial data output
Serial-in, parallel-out, shift register
Serial data input
Parallel data output
Parallel-in, parallel-out, shift register
Parallel data input
Parallel data output
Parallel-in, serial-out, shift register
Serial data output
Parallel data input

## Slide 18: Serial-in, Serial-out, Shift-right, Shift register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
Serial Input
CLK
Serial output
Using D Flip-flop
Data = 1010
0
0
1
0
1
0
0
1
0
1
1
0
1
0
Q1’
Q2’
Q3’
Q4’

## Slide 19: Serial-in, Serial-out, Shift-right, Shift register
Using JK Flip-flop
Data = 1010
FF1
J1
Q1
>
FF2
J2
Q2
>
FF3
J3
Q3
>
FF4
J4
Q4
>
Serial Input
CLK
Serial output
0
1
0
1
K1
K2
K3
K4
Q1’
Q2’
Q3’
Q4’
0
1
0
1
1
0
0
1
1
0
0
1
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
0

## Slide 20: Serial-in, Parallel-out, Shift register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
Serial Input
CLK
QA
QB
QC
QD

## Slide 21: Parallel-in, Parallel-out, Shift register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
A
CLK
B
C
D
QA
QB
QC
QD

## Slide 22: Parallel-in, Serial-out, Shift register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
Shift/
CLK
A
B
C
D
0
0
1
0
1
1
1
1
1
0
1
0
0
1
0
1
1
1
1
1
1
0
1
1
0
1
0

## Slide 23: Asynchronous Counter
Section - 3

## Slide 24: Asynchronous Counters v/s Synchronous Counters
Asynchronous Counters | Synchronous Counters
In this type of counters FFs are connected in such a way that the output of the first FF drives the clock for the second FF, the output of the second the clock of the third and so on. | In this type of counters there is no connection between the output of first FF and clock input of next FF and so on.
All the FFs are not clocked simultaneously. | All the FFs are clocked simultaneously.
Design and implementation is very simple even for more number of states. | Design and implementation becomes tedious and complex as the number of states increases.
Main drawback of these counters is their low speed as the clock is propagated through a number of FFs before it reaches the last FF. | Since clock is applied to all the FFs simultaneously the total propagation delay is equal to the propagation delay of only one FF. Hence they are faster.

## Slide 25: 2-bit Ripple Up-Counter using Negative Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
 | 0 | 0 | 0 | 1
 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1
 | 1 | 1 | 0 | 0
CLK
Q1
Q2
0
1
0
1
0
0
1
0

## Slide 26: 2-bit Ripple Down-Counter using Negative Edge-triggered Flip-Flop
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
 | 0 | 0 | 1 | 1
 | 1 | 1 | 1 | 0
 | 1 | 0 | 0 | 1
 | 0 | 1 | 0 | 0
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK
Q1
Q2
0
1
0
1
0
0
1
0
Q1’
1
0
1
0
1

## Slide 27: 2-bit Ripple Up-Counter using Positive Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
 | 0 | 0 | 0 | 1
 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1
 | 1 | 1 | 0 | 0
CLK
Q1
Q2
0
0
0
1
0
0
1
1
1
Q1’
1
1
1
0
0
0

## Slide 28: 2-bit Ripple Down-Counter using Positive Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
 | 0 | 0 | 1 | 1
 | 1 | 1 | 1 | 0
 | 1 | 0 | 0 | 1
 | 0 | 1 | 0 | 0
CLK
Q1
Q2
0
0
0
1
0
0
1
1
1

## Slide 29: Mod-6 Asynchronous Counter
After pulses | State |  |  | Reset(R)
 | Q3 | Q2 | Q1 | 
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
2 | 0 | 1 | 0 | 0
3 | 0 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0
5 | 1 | 0 | 1 | 0
6 | 1 | 1 | 0 | 1
 | ↓ | ↓ | ↓ | 
 | 0 | 0 | 0 | 0
 | 0 | 0 | 1 | 0
R = 0 for 000 to 101
R = 1 for 110
R = x for 111
R = Q3Q2Q1’ + Q3Q2Q1
R = Q3Q2

## Slide 30: Mod-6 Asynchronous Counter
FF1
T1
Q1
>
Q1’
FF2
T2
Q2
>
Q2’
FF3
T3
Q3
>
Q3’
1
Q1
Q2
1
1
Q3
R’
CLK

## Slide 31: Synchronous Counter
Section - 4

## Slide 32: Design of Synchronous Counters
Step 1 - Number of flip-flops: Based on the description of the problem, determine the required number n of the FFs - the smallest value of n is such that the number of states N ≤ 2n and the desired counting sequence.
Step 2 - State diagram: Draw the state diagram showing all the possible states.
Step 3 - Choice of flip-flops and excitation table: Select the type of flip-flops to be used and write the excitation table. An excitation table is a table that lists the present state (PS), the next state (NS) and the required excitations.
Step 4 - Minimal expressions for excitations: Obtain the minimal expressions for the excitations of the FFs using K-maps for the excitations of the flip-flops in terms of the present states and inputs.
Step 5 - Logic Diagram: Draw the logic diagram based on the minimal expressions.

## Slide 33: Excitation Tables
PS | NS | Required inputs | 
Qn | Qn+1 | S | R
0 | 0 | 0 | x
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | x | 0
S-R FF
PS | NS | Required inputs | 
Qn | Qn+1 | J | K
0 | 0 | 0 | x
0 | 1 | 1 | x
1 | 0 | x | 1
1 | 1 | x | 0
J-K FF

## Slide 34: Excitation Tables
PS | NS | Required inputs
Qn | Qn+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
D FF
T FF
PS | NS | Required inputs
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 35: Design of Synchronous 3-bit Up Counters
Step 1 - Number of flip-flops:
A 3-bit up-counter requires 3 flip-flops. The counting sequence is 000, 001, 010, 011, 100, 101, 110, 111, 000 …
Step 2 - Draw the state diagram:
000
001
010
011
100
101
110
111

## Slide 36: Design of Synchronous 3-bit Up Counters
Step 3 - Select the type of flip-flops and draw the excitation table:
JK flip-flops are selected and the excitation table of a 3-bit up-counter using J-K flip-flops is drawn as shown below.
PS |  |  | NS |  |  | Required excitations |  |  |  |  | 
Q3 | Q2 | Q1 | Q3 | Q2 | Q1 | J3 | K3 | J2 | K2 | J1 | K1
0 | 0 | 0 | 0 | 0 | 1 | 0 | x | 0 | x | 1 | x
0 | 0 | 1 | 0 | 1 | 0 | 0 | x | 1 | x | x | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | x | x | 0 | 1 | x
0 | 1 | 1 | 1 | 0 | 0 | 1 | x | x | 1 | x | 1
1 | 0 | 0 | 1 | 0 | 1 | x | 0 | 0 | x | 1 | x
1 | 0 | 1 | 1 | 1 | 0 | x | 0 | 1 | x | x | 1
1 | 1 | 0 | 1 | 1 | 1 | x | 0 | x | 0 | 1 | x
1 | 1 | 1 | 0 | 0 | 0 | x | 1 | x | 1 | x | 1
PS | NS | Required inputs | 
Qn | Qn+1 | J | K
0 | 0 | 0 | x
0 | 1 | 1 | x
1 | 0 | x | 1
1 | 1 | x | 0
J-K FF Excitation Table

## Slide 37: Design of Synchronous 3-bit Up Counters
Step 4 - Obtain the minimal expressions:
From excitation table, J1 = K1 = 1.
K – Maps for excitations J3, K3, J2 and K2 and their minimized form are as follows:
Q3Q2
Q1
00
10
0
1
01
11
1
x
x
x
x
J3 = Q2Q1
Q3Q2
Q1
00
10
0
1
01
11
1
x
x
x
x
K3 = Q2Q1

## Slide 38: Design of Synchronous 3-bit Up Counters
Q3Q2
Q1
00
10
0
1
01
11
1
x
1
x
J2 = Q1
Q3Q2
Q1
00
10
0
1
01
11
1
x
x
x
x
K2 = Q1
1
x
x

## Slide 39: Design of Synchronous 3-bit Up Counters
Step 5 - Draw the logic diagram:
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
FF3
J3
Q3
>
K3
Q3’
CLK

## Slide 40: Sequential Generator
Section - 5

## Slide 41: Sequence Generator/Pulse Train Generators (Direct Logic)
Example: Generate the following pulse train using direct logic.
0
1
1
1
0
1
1
1
0
FF States
0
1
3
5
State assignment
State diagram
 | LSB
0
1
1
1
0
0
1
?
FF States |  |  | Decimal equivalent
 |  | LSB | 
0
1
1
1
0 | 0
0 | 0
0 | 1
1 | 0
0
1
3
5

## Slide 42: Sequence Generator (Direct Logic)
PS |  |  | NS |  |  | Required excitations |  |  |  |  | 
Q3 | Q2 | Q1 | Q3 | Q2 | Q1 | J3 | K3 | J2 | K2 | J1 | K1
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | X | 1 | X
0 | 0 | 1 | 0 | 1 | 1 | 0 | X | 1 | X | X | 0
0 | 1 | 1 | 1 | 0 | 1 | 1 | X | X | 1 | X | 0
1 | 0 | 1 | 0 | 0 | 0 | X | 1 | 0 | X | X | 1
J3 = Q2
K3 = 1
J2 = Q3’Q1
K2 = 1
J1 = 1
K1 = Q3

## Slide 43: Sequence Generator (Direct Logic)
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
CLK
FF3
J3
Q3
>
K3
Q3’
1
1

## Slide 44: Sequence Generator (Indirect Logic)
Example: Generate the following pulse train using indirect logic.
0
1
1
0
1
0
1
1
0
1
1
Q3 | Q2 | Q1 | Output(f) | States
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 2
0 | 1 | 1 | 1 | 3
1 | 0 | 0 | 0 | 4
1 | 0 | 1 | X | 5
1 | 1 | 0 | X | 6
1 | 1 | 1 | X | 7
Q3Q2
Q1
00
10
0
1
01
11
1
x
x
x
f = Q2 + Q3’ Q1’
1
1

## Slide 45: Sequence Generator (Indirect Logic)
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
FF3
J3
Q3
>
K3
Q3’
1
1
1
CLK
f