## Slide 1: Unit-5 Memories and Programmable Logic Devices
krunal.vyas@darshan.ac.in
9601901005
Computer Science & Engineering
Prof. Krunal D Vyas
Digital Fundamentals (DF)
DU #2101CS303

## Slide 2

Looping
Outline
  Memory organization and operation
  Classification of memory: ROM, RAM, ROM as PLD
  Programmable Array Logic (PAL)
  Programmable Logic Array (PLA)

## Slide 3: Memory organization and operation
Section - 1

## Slide 4: Memory organization and operation
Memory
Bidirectional data bus
Address bus
R/
(Read/write control)
CS
(chip select)
Mainly two types of operations
Write operation
Read operation

## Slide 5: Memory Expansion
RAM 1
16 x 4
A3
A2
A1
A0
D3
D2
D1
D0
R/
RAM 2
16 x 4
A3
A2
A1
A0
D3
D2
D1
D0
R/
A3
A2
A1
A0
R/
D7
D6
D5
D4
D3
D2
D1
D0
Example:- Show how to combine several 16 x 4 RAM to form a 16 x 8 RAM.

## Slide 6: Memory Expansion
Example:- Show how to combine several 1K x 8 PROMs to produce 4K x 8 PROM.
Solution:-
  1K x 8 PROM has 10 number of address lines because 210 = 1024 (1K).
  We need total 4 number of 1K x 8 PROM chips to make one 4K x 8 PROM chip.
PROM 1
1K x 8
PROM 1
1K x 8
PROM 1
1K x 8
PROM 1
1K x 8
D7
D0
A9
A0
A10
A11
2 to 4 decoder
O0
O1
O2
O3

## Slide 7: Memory Expansion
A11
A10
A9
A8
A7
A6
A5
A4
A3
A2
A1
A0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
Memory chip | Starting address | Ending address
PROM 1 | 000 H | 3FF H
PROM 2 | 400 H | 7FF H
PROM 3 | 800 H | BFF H
PROM 4 | C00 H | FFF H

## Slide 8: Classification of memory: ROM, RAM, ROM as PLD
Section - 2

## Slide 9: Read-Only Memory (ROM)
A read-only memory (ROM) is essentially a memory device in which permanent binary information is stored.
The binary information must be specified by the designer and is then embedded in the unit to form the required interconnection pattern.
Once the pattern is established, it stays within the unit when the power is turned off and on again.
A ROM which can be programmed is called a PROM. The process of entering information in a ROM is known as programming.
ROMs are used to store information which is of fixed type, such as tables for various functions, fixed data and instructions.
ROMs can be used for designing combinational logic circuits.

## Slide 10: Read-Only Memory (ROM)
Advantages of using a ROM as a PLD
  Ease of design since no simplification or minimization of logic function is required
  Designs can be changed, modified easily
  Faster than discrete MSI/SSI circuit
  Cost is reduced
Disadvantages of ROM based circuits
  Non-utilization of complete circuit
  Increased power requirement
  Enormous increase in size with increase in number of input variables

## Slide 11: ROM Organization
k inputs – provide address for the memory
n outputs – data bits of the stored word selected by address
k address input lines specify 2k words
ROM does not have data inputs because it does not have write operation.
2k x n
ROM
k inputs (address)
n outputs (data)

## Slide 12: ROM Organization (32 x 8 ROM)
I0
I1
I2
I3
I4
A0
A1
A2
A3
A4
A5
A6
A7
0
1
2
3
28
29
30
31
•
•
•
5 x 32 decoder
Internal logic of 32 x 8 ROM

## Slide 13: ROM Organization (32 x 8 ROM)
The unit consists of 32 words of 8 bits each.
There are five input lines that form the binary numbers from 0 through 31 for the address.
The five inputs are decoded into 32 distinct outputs by means of a 5 x 32 decoder.
Each output of the decoder represents a memory address.
The 32 outputs of the decoder are connected to each of the 8 OR gates.
Each OR gate must be considered as having 32 inputs.
Since each OR gate has 32 input connections and there are 8 OR gates, the ROM contains 32 x 8 = 256 internal connections.
In general, a 2k x n ROM will have an internal k x 2k decoder and n OR gates.
Each OR gate has 2k inputs, which are connected to each of the outputs of the decoder.

## Slide 14: ROM Organization Example
Implement following functions using ROM.
F1 = ∑ m(1, 3, 4, 6), F2 = ∑ m(2, 4, 5, 7), F3 = ∑ m(0, 1, 5, 7), F4 = ∑ m(1, 2, 3, 4)
0
1
2
3
4
5
6
7
A2
A1
A0
3 x 8
decoder
F1
F2
F3
F4
A2 | A1 | A0 | F1 | F2 | F3 | F4
0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1 | 0

## Slide 15: ROM Organization Exercise
1) Design a combinational circuit using a PROM. The circuit accepts 3-bit binary number and generates its equivalent XS-3.
2) Realize two outputs F1 and F2 using a 4 x 2 PROM:
          F1 (A1, A0) = ∑ m(0, 2)
          F2 (A1, A0) = ∑ m(0, 1, 3)

## Slide 16: Mask programmable ROM
Programmed at the time of manufacturing, as the last process of fabrication.
Custom programmed or mask programmed.
Data can’t be changed after fabrication.
Only for bulk production.

## Slide 17: Programmable ROM (PROM)
Programmed by the user using a special circuit – PROM programmer.
It can be programmed only once after which its contests are permanently fixed as in a ROM.
Suitable for storage of data which is of permanent in nature.
Available without any data on it from vendor.

## Slide 18: Erasable PROM (EPROM)
It can be programmed again and again, so referred as erasable and programmable ROM.
Two techniques: Ultraviolet radiation, Electrically
A ROM in which erasing process using ultraviolet radiation is used is known as EPROM.
The device using electrical voltage for erasing is known as Electrically EPROM or Electrically alterable ROM (EAROM)

## Slide 19: Random access memory (RAM)
Used in computers for the temporary storage of programs and data.
Read and write both operations are performed by RAM which requires fast cycle times as not to slow down the computer operation.
It is volatile and lose all stored information if power is interrupted or turned off.
RAMs typically come with word capacities of 1K, 4K, 8K, 16K, etc.. and word sizes of 1, 4 or 8-bits.
It can be expanded by combining several memory chips.

## Slide 20: SRAM v/s DRAM
Static RAM | Dynamic RAM
SRAM has lower access time, so it is faster compared to DRAM. | DRAM has higher access time, so it is slower than SRAM.
SRAM is costlier than DRAM. | DRAM costs less compared to SRAM.
SRAM requires constant power supply, which means this type of memory consumes more power. | DRAM offers reduced power consumption, due to the fact that the information is stored in the capacitor.
Due to complex internal circuitry, less storage capacity is available compared to the same physical size of DRAM memory chip. | Due to the small internal circuitry in the one-bit memory cell of DRAM, the large storage capacity is available.
SRAM has low packaging density. | DRAM has high packaging density.
No need to refresh periodically. | Due to capacitor used as storage element, information may lose over period of time. So, need to refresh periodically.
Uses an array of 6 transistors for each memory cell. | Uses a single transistor and capacitor for each memory cell.

## Slide 21: RAM v/s ROM
 | RAM | ROM
Data | The data is not permanent but it can be altered any number of times. | The data is permanent. It can be altered but only a limited number of times that too at slow speed.
Speed | It is a high-speed memory. | It is much slower than the RAM.
CPU Interaction | The CPU can access the data stored on it. | The CPU can not access the data stored on it. In order to do so, the data is first copied to the RAM.
Size and Capacity | Large size with higher capacity. | Small size with less capacity.
Usage | Primary memory (DRAM DIMM modules), CPU Cache (SRAM). | Firmware like BIOS or UEFI. RFID tags, microcontrollers, medical devices, and at places where a small and permanent memory solution is required.
Cost | It doesn’t come cheap. | Way cheaper than RAM.

## Slide 22: Programmable Array Logic (PAL)
Section - 3

## Slide 23: Programmable Array Logic (PAL)
Programmable array logic (a registered trade mark of Monolithic Memories) is a particular family of programmable logic devices (PLDs) that is widely used and available from a number of manufacturers.
The PAL circuits consist of a set of AND gates whose inputs can be programmed and whose outputs are connected to an OR gate, i.e. the inputs to the OR gate are hard-wired.
The PAL is easier to program as only the AND gates are programmable.
The fuse symbols represent fusible links that can be burned open using equipment similar to a PROM programmer.
Note that every input variable and its complement can be left either connected or disconnected from every AND gate.
C
B
A
Programmable AND gates
Output
fuse symbol

## Slide 24: Ex: F = AB’C + A’BC using PAL
Figure shows how the circuit is programmed to implement F = A’BC + AB’C.
All input variables and their complements are left connected to the unused AND gate, whose output is, therefore, AA’BB’CC’ = 0.
The 0 has no affect on the output of the OR gate.
C
B
A
Programmable AND gates
AB’C
A’BC
0
Unused
F = AB’C + A’BC

## Slide 25: PAL – Second method
A
B
C
Fixed OR array
Programmable AND array
F1
F2

## Slide 26: Example:- F1 = A’BC + AC’ + AB’C, F2 = A’B’C’ + BC using PAL.
A
B
C
Fixed OR array
Programmable AND array
F1
F2

## Slide 27: PAL Example
Implement the following Boolean functions using PAL with four inputs and 3-wide AND-OR structure. Also write the PAL programming table.
  F1(A, B, C, D) =
  F2(A, B, C, D) =
  F3(A, B, C, D) =
  F4(A, B, C, D) =

## Slide 28: PAL Example
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
1
1
1
1
1
1
F1 = ABC’ + A’B’CD’
F2 = A + BCD

## Slide 29: PAL Example
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
F3 = CD + A’B + B’D’
AB
CD
00
10
00
01
0
1
2
3
01
11
4
5
6
7
11
10
12
13
14
15
8
9
10
11
1
1
1
F4 = ABC’ + AC’D’ + A’B’C’D + A’B’CD’
= F1 + AC’D’ + A’B’C’D
1
1
1
1
1
1
1
1
1
1

## Slide 30
Product term | AND Inputs |  |  |  |  | Outputs
 | A | B | C | D | F1 | 
1 | 1 | 1 | 0 | - | - | F1 = ABC’ + A’B’CD’
2 | 0 | 0 | 1 | 0 | - | 
3 | - | - | - | - | - | 
4 | 1 | - | - | - | - | F2 = A + BCD
5 | - | 1 | 1 | 1 | - | 
6 | - | - | - | - | - | 
7 | 0 | 1 | - | - | - | F3 = CD + A’B + B’D’
8 | - | - | 1 | 1 | - | 
9 | - | 0 | - | 0 | - | 
10 | - | - | - | - | 1 | F4 = F1 + AC’D’ + A’B’C’D
11 | 1 | - | 0 | 0 | - | 
12 | 0 | 0 | 0 | 1 | - | 

## Slide 31
A
B
C
Fixed OR array
Programmable AND array
F1
F2
D
F1
F3
F4
F1 = ABC’ + A’B’CD’
F2 = A + BCD
F3 = CD + A’B + B’D’
F4 = F1 + AC’D’ + A’B’C’D

## Slide 32: PAL Exercise
Realize the following functions using a PAL with four inputs and 3-wide AND-OR structure. Also write the PAL programming table.
  F1(A, B, C, D) =
  F2(A, B, C, D) =
  F3(A, B, C, D) =
  F4(A, B, C, D) =

## Slide 33: Programmable Logic Array (PLA)
Section - 4

## Slide 34: Programmable Logic Array (3-input 4-output PLA)
The PLA combines the characteristics of the PROM and the PAL by providing both a programmable OR array and a programmable AND array, i.e. in a PLA both AND gates and OR gates have fuses at the inputs.
A third set of fuses in the output inverters allows the output function to be inverted if required.
A
B
C
Programmable AND gates
Programmable OR gates
Out-1
Out-2
Out-3
Out-4

## Slide 35: PLA Example
Implement the following two Boolean functions with a PLA:
F1(A, B, C) = , F2(A, B, C) =
AB
C
00
10
0
1
0
1
2
3
01
11
4
5
6
7
1
1
1
1
AB
C
00
10
0
1
0
1
2
3
01
11
4
5
6
7
0
0
0
0
F1 (T) = A’C’ + B’C’ + A’B’
F1 = (A’+B’) (B’+C’) (A’+C’)
F1’ = AB + AC + BC
F1(C) = (AB + AC + BC)’

## Slide 36
AB
C
00
10
0
1
0
1
2
3
01
11
4
5
6
7
1
1
1
1
AB
C
00
10
0
1
0
1
2
3
01
11
4
5
6
7
0
0
0
0
F2 (T) = A’B’C’ + AB + AC
F2 = (A+B’) (A+C’) (A’+B+C)
F2’ = A’B + A’C + AB’C’
F2(C) = (A’B + A’C + AB’C’)’
Product term |  | Inputs |  |  | Outputs | 
 |  | A | B | C | F1(C) | F2(T)
1 | AB | 1 | 1 | - | 1 | 1
2 | AC | 1 | - | 1 | 1 | 1
3 | BC | - | 1 | 1 | 1 | -
4 | A’B’C’ | 0 | 0 | 0 | - | 1

## Slide 37
C
B
A
F1(C) = (AB + AC + BC)’
F2 (T) = A’B’C’ + AB + AC
1
0
F1
F2
AB
AC
BC
A’B’C’

## Slide 38: Exercise
Implement following Boolean functions using PLA.
F1 = A’B + AC’ + A’BC’
F2 = (AC’ + B’C)’